## Slide 1
Advisor
Ashish Pujari
Failure Detection for
Pharmaceutical Cold Chain Logistics
Client
Presented By
Amily Huang
Jenny Jiang
Duo Zhou

## Slide 2
Reducing the failed shipment ratio is a long-sought objective for pharmaceutical cold chain industry
Find solutions that can ultimately help to predict and mitigate failures during a shipment
“Pharmaceutical manufacturers lose 15 billion per year due to cold chain failure”
Problem Statement
3

## Slide 3
01
Pharmaceuticals do not experience temperature deviation
02
Container has no critical parts failure
03
Container is performing according to design
What is a safe delivery of shipment?
2

## Slide 4
Predictive Model
Predict the likelihood of temperature deviation given certain order information
Help the company to give pin-pointed handling instructions, or reconsider flight routes for a shipment when a prediction of high likelihood of failure is given
SAFE
Failure Risk Profile
Identify failure root causes to different types of failures
    Identify major container handling behaviors that lead to high failure rate
Understand the circumstances when failure happens
Goal of Analysis
4
Notes: Standardize and improve training process to lower improper handling related failure and reduce cost
Identify top airlines and trade lanes that have high failure rate

## Slide 5
Integrated using container number and order number
Each observation contains information regarding a unique container movement from origin to destination
Container movement for 3 years
Jan 2018 - Feb 2021
70k+
Data Overview
Container Logged Data
Trade lane &
Shipment Data
Reported Incidents
Data
Supplementary
Data
5

## Slide 6
Failure (Label) Definition
Variable Aggregation
Row Selection
Failure Risk Profile
Colinearity Analysis
Feature Engineering
Imbalanced Data Handling
Model Implementation
Model Evaluation
Recommendation
Analytics Workflow
Data Preparation
Descriptive Analysis
Predictive Model
SAFE
6
Notes: Anomaly = under+over

## Slide 7
7
Temperature Deviation
Average container inside temperature deviates from the set temperature range
Parts Failure Alarms
Essential parts alarms are triggered
Compressor Performance Anomalies
Container compressor is not functioning properly
Data Preparation
Descriptive Analysis
Recommendation
Predictive Model
Failure Definition
Label
Binary: Failure (1) vs. Normal (0)
This definition of temperature deviation(TD) was validated using actual reported TD data
Compressor is a critical part and more frequently utilized
7
Notes: The details of the comparison and validation are displayed in the appendix

## Slide 8
Extract 1,673 anomaly observations using Copula Quantile Regression
Compressor Power Step vs. Delta
Distribution
1673 observations
Total Anomaly
Copula quantile regression 5% and 95%
Method
Over-performing: Delta is low, but compressor power step is high
Under-performing: Delta is high, but compressor power step is low
Definition
Failure Definition - Compressor Performance Anomalies
Data Preparation
Descriptive Analysis
Recommendation
Predictive Model
8
Notes: Delta will be discussed in next slides

## Slide 9
Variable Aggregation & Row Selection
Data Preparation
Descriptive Analysis
Recommendation
Predictive Model
Row Selection
Only records with container logged information are selected
Only shipments with operational log time duration larger than 8 hours are chosen to avoid average inside temperature values being over influenced by container’s preconditioning period
Variable Aggregation
Out of Design Temperature Exposure Duration (ODTD)
Average Weighted Ambient Temperature (AWAT)
Delta (AWAT - Set Temperature)
9

## Slide 10
Descriptive Analysis
10

## Slide 11
Failure Risk Profile
Descriptive Analysis
Data Preparation
Recommendation
Predictive Model
Profile 1
Validation of self defined TD using reported
Temperature Deviation (TD)
Risk Profile
Compressor
Heater
Charger
Failure Alarms
Risk Profile
Compressor Performance Anomaly Risk Profile
Profile 2
Profile 3
11

## Slide 12
Temperature Deviation (TD) Risk Profile
Descriptive Analysis
Data Preparation
Recommendation
Predictive Model
Season
Summer has the highest TD rate, taking up 39% of the total TD
Delta
TD rate increases exponentially when |Delta| is above 10°C
Out of designed temperature exposure duration (ODTD)
TD rate reaches 70% when ODTD is above 5 hours
Shipment Duration
The longer the shipment duration, the higher the TD rate
Higher ambient temperature and longer exposure to extreme temperature increase TD rate
12

## Slide 13
Temperature Deviation (TD) Risk Profile
Descriptive Analysis
Data Preparation
Recommendation
Predictive Model
Number of door openings
TD rate climbs after 3 times of door openings
Battery Mean
TD rate increases when battery mean is below 70%
Economic Status of origin and destination countries
TD increases when the origin is developing country
10.6%
Developed → Developed
9.6%
Developed → Developing
16.1%
Developing → Developed
17.2%
Developing → Developing
More door openings and lower battery mean increase TD rate
13

## Slide 14
Failure Alarms Risk Profile
Descriptive Analysis
Data Preparation
Recommendation
Predictive Model
A
l
a
r
m
R
a
t
e
S
p
r
i
n
g
S
u
m
m
e
r
A
u
t
u
m
n
W
i
n
t
e
r
C
o
m
p
r
e
s
s
o
r
0
.
2
1
%
0
.
4
4
%
0
.
2
5
%
0
.
2
8
%
H
e
a
t
e
r
0
.
0
6
%
0
.
2
0
%
0
.
0
4
%
0
.
0
6
%
Compressor & Heater Alarms
Season
Summer takes up 39% of total compressor alarms and 56% of total heater alarms
Delta
Compressor alarm rate increases as Delta gets larger
Shipment Duration
The longer the shipment duration, the higher the compressor & heater alarm rate
Out of designed temperature exposure duration (ODTD)
Compressor alarm rate jumps after 4 hrs of ODTD
Heater alarm rate increases sharply after 10 hrs of ODTD
Number of door openings
Compressor & heater rate increases after 6 times of door openings
Higher ambient temp., longer exposure to extreme temp., and more door openings increase alarm rate
14
Notes: Supply Voltage:
Compressor and heater alarms are more likely to occur in summer
Charger alarm rate peaks when container is exposed to a supply voltage of 100V-127V in origin and destination

## Slide 15
Charger Alarms
Failure Alarms Risk Profile
Descriptive Analysis
Data Preparation
Recommendation
Predictive Model
Supply Voltage
Charger alarm rate peaks when the supply voltage is 100V-127V in origin and destination
0.65%
100V-127V
100V-127V
Origin Voltage
Destination Voltage
0.32%
220V-240V
220V-240V
Charging Behavior
Not continuously charging the container
Frequently alternating between charging and no charging
Supply voltage of 100V-127V and incorrect charging behavior increase charger alarm rate
15
Notes: Charger alarm rate doubles when the supply voltage is 100 – 127volt
Supply Voltage:
Compressor and heater alarms are more likely to occur in summer
Charger alarm rate peaks when container is exposed to a supply voltage of 100V-127V in origin and destination

## Slide 16
Compressor Alarm Rate
Mean Number of Door Openings
Mean Battery Level
Temperature Deviation Rate
Charging Time Ratio
Out of Designed Temperature
Exposure (hrs)
Normal
Abnormal
13%
35%
0.045
0.119
80%
71%
3.5
4.4
0.3%
1.1%
47%
40%
Descriptive Analysis
Data Preparation
Recommendation
Predictive Model
Compressor Performance Anomalies Risk Profile
Containers with compressor performance issue tend to have more compressor alarm rate & TD rate
16

## Slide 17
Predictive Model
17

## Slide 18
Predictive Model
Data Preparation
Recommendation
Descriptive Analysis
Feature Engineering
Label Selection
Temperature deviation (TD)
Reason: The ultimate objective is to avoid temperature deviation during a shipment
Predictors Selection
Features whose values are given or can be estimated at the beginning of each shipment
Season
Set Temperature
Estimated Shipment Duration
Estimated AWAT
Usage
Origins and Destinations
Airlines
Recategorization
To avoid over dimensionalities of following categorical features
Origins and Destinations – Recategorized into 4 groups by economic status
Airlines- Recategorized into 3 groups by number of container shipments with Envirotainer
18

## Slide 19
Main reason to create balanced dataset: Give equal priority to each class
Predictive Model
Data Preparation
Recommendation
Descriptive Analysis
 | Adaptive Resampling |  | Cost-sensitive learning
 | Oversampling | Down-sampling | 
Concept |  |  | 
Advantage | no loss of information | reduce run-time and memory | no loss of information
Disadvantage | prune to overfit than down-sampling | lose critical information and create bias | 
No TD
TD
TD
No TD
Original Dataset
Final Dataset
SMOTE
No TD
TD
No TD
TD
Original Dataset
Final Dataset
No TD
TD
Original Dataset
:
=
7.3 : 1
Weights for cost function
88%
12%
Random down-sampling
Imbalanced Data Handling
19

## Slide 20
Predictive Model
Data Preparation
Recommendation
Descriptive Analysis
Model Implementation & Evaluation
Algorithms Implemented
Logistic Regression
XGBoost
Artificial Neural Network (ANN)
Evaluation Metrics
Model Overfitting
Recall
  AUC score
  Failures rarely occur but costly
  It preferred to over predict failures to place extra caution and failure preventative measures
Measures how much the model is capable of distinguishing between classes
Higher the AUC score, the better the model is at predicting 0s as 0s and 1s as 1s
Data was split into train (67.5%), validation (22.5% ), and test (10%) sets
20

## Slide 21
Model Implementation – Overfitting Analysis
Predictive Model
Data Preparation
Recommendation
Descriptive Analysis
Cost sensitive learning performed best for both XGBoost and ANN
However, ANN with cost-sensitive learning performed much better in the convergence progression between train and validation AUC scores than XGBoost.
Cost-Sensitive Learning | XGBoost | ANN
Loss Curve |  | 
AUC Curve |  | 
Training Loss
Validation Loss
Number of Gradient Boosted Trees
Number of Gradient Boosted Trees
Epochs
Epochs
21

## Slide 22
Validation set
AUC & Recall Scores
Predictive Model
Data Preparation
Recommendation
Descriptive Analysis
Recall Score | Logistic Regression | XGBoost | ANN
Original data | 0.298 | 0.486 | 0.484
Oversampling with SMOTE | 0.821 | 0.590 | 0.825
Random down-sampling | 0.820 | 0.878 | 0.891
Cost sensitive learning | 0.821 | 0.878 | 0.891
AUC Score | Logistic Regression | XGBoost | ANN
Original data | 0.876 | 0.931 | 0.936
Oversampling with SMOTE | 0.889 | 0.920 | 0.930
Random down-sampling | 0.887 | 0.927 | 0.928
Cost sensitive learning | 0.888 | 0.931 | 0.936
22
Winning Model
Test Set
Accuracy: 0.8641
Precision: 0.472
Recall Score: 0.891
F1 Score: 0.61
AUC score 0.936
Artificial Neural Network with cost-sensitive learning
Highest Recall with Good AUC Scores
22

## Slide 23
Model Interpretability
Predictive Model
Data Preparation
Recommendation
Descriptive Analysis
XGBoost is more interpretable that ANN
Shipment Duration and Delta (AWAT-Set Temp) have the most impact on failure occurrence.
Chart: Top 10 Predictors of XGBoost with Cost-sensitive Learning
| Origin - Destination Continent: NA-AS | Origin - Destination Country Status: Developed Country - Developing Country | Origin - Destination Continent: NA-NA | Origin - Destination Continent: NA-EU | Origin - Destination Continent: EU-AS | Weighted Average Ambient Temperature (°C) | Origin - Destination Continent: EU-NA | Origin - Destination Continent: EU-OC | Set Temperature | Shipment Duration
Feature Importance | 0.02474 | 0.030803 | 0.031609 | 0.034001 | 0.046021 | 0.059232 | 0.067424 | 0.094421 | 0.10237 | 0.14693
23

## Slide 24
Recommendation
24

## Slide 25
01
03
05
04
02
Recommendation
Place containers into temperature-controlled storages during transition
Turn on the container no more than 2 hours before placing the product inside
Minimize the during a shipment, under 5 times if possible
Continuously charge and maintained the battery level above 70% if possible
Use voltage transformers when the supply voltage is between 100V - 127V or consider a charger design modification
25
Notes: 看要不要把這句刪掉, 前面charging alarm已經有說到了
do not frequently alternate between charging and not charging
這句話可以用講的~ 這樣slide也看起來更清晰

## Slide 26
Release Month | May
Set Temp (°C) | 5 °C
Average Ambient Temperature(°C) | 22 °C
Shipment duration | 200hrs
Origin - Destination | ATL - DEL
Airlines | Delta Air Lines (Big Airlines)
Demo
26
Predictive Model
Place an Order
Step 1
Step 2
Step 3
Step 4
Recommended Preventative Measures
The classification
is TD

## Slide 27
01
03
04
02
Future Works
Utilizing historical and streaming data to give real time or near real time predictions on different types of failures
Establishing a resource/logistic allocation system based on the derived insights on shippers, airlines, routes and transfer hubs
Generating real time/near real time solutions, i.e. maintenance, repair or replacement, using both real time failure prediction and resource allocation systems
25
Developing demand related analytics and forecast based on historical ordering data, order back-log data and real time health events.
Notes: 看要不要把這句刪掉, 前面charging alarm已經有說到了
do not frequently alternate between charging and not charging
這句話可以用講的~ 這樣slide也看起來更清晰

## Slide 28
Thank You!
27

## Slide 29
Appendix
28

## Slide 30
Season vs. Temperature Deviation Rate
Temperature deviation often happens in summer
Reported temperature deviations show the same trend against the season factor
Temperature Deviation Findings
29

## Slide 31
Delta vs. Temperature Deviation Rate
When the Delta is extremely high or low, the temperature deviation rate is 100%
The temperature deviation rate minimizes when Delta is between -10°C and 10°C and starts to exponentially increase when Delta is over 10°C or below -10°C.
Temperature Deviation Findings
30

## Slide 32
Out of Designed Temperature Duration vs. Temperature Deviation
When the ODTD increases from 0 hour to 10 hours, the cumulative temperature deviation rate significantly increases from 0.11 to 0.87.
Temperature Deviation Findings
31

## Slide 33
Shipment Duration vs. Temperature Deviation
Temperature deviation rate increases from 0.01 to 0.08 when the shipment duration changes from less than 5 days to less than 10 days
Temperature Deviation Findings
32

## Slide 34
Compressor Power Step vs. Temperature Deviation
Containers experience higher temperature deviation rate when power step used for compressor (workload) increase
The reported temperature deviation rate demonstrates a very similar trend as its self-defined counterpart when plotted against mean compressor power step.
Temperature Deviation Findings
33

## Slide 35
Number of Door Openings vs. Temperature Deviation
The number of door openings between 0 to 7 times, the temperature deviation rate increases from 0.06 to 0.32
The temperature deviation rate climbs significantly when the number of door openings is above 3 times during a shipment.
Temperature Deviation Findings
34

## Slide 36
Battery Mean vs. Temperature Deviation
The non-temperature deviation shipments’ battery mean is 83.82%, and temperature deviated shipments’ battery mean is 46.19%
Temperature deviation rate decreases as the battery mean increases
Temperature Deviation Findings
35

## Slide 37
Battery < 30% vs. Temperature Deviation
As the duration ratio of battery less than 30% increases, the temperature deviation rate will also increase
It is suggested not to keep the container battery less than 30%.
Temperature Deviation Findings
36

## Slide 38
Charging Duration vs. Cumulative Temperature Deviation Rate
The longer we charge containers during a shipment, the lower temperature deviation rate will be
Temperature Deviation Findings
37

## Slide 39
Economic Status vs. Temperature Deviation
Economic status of origin countries has a higher impact on temperature deviation ratio as the airline that handles the shipment tend to come from the origin country
Developed country airlines tend to handle containers better and produce smaller TD ratios
Temperature Deviation Findings
38

## Slide 40
Top 3 Airline vs. Container Handling Behaviors
The top 3 temperature deviation rate airlines have a lower battery mean than non-temperature deviated shipments
The battery less than 30% and 0% duration are higher, while the charging duration rate is lower than non-temperature deviation shipments
The average number of door openings is higher for those airlines than the non-temperature deviation shipments.
Airlines with High Temperature Deviation Rate
39

## Slide 41
Top 3 Trade Lanes vs. External Uncontrollable Factors
Shipment trade lanes with the highest temperature deviation rate tend to have a much larger average Delta than trade lanes with low temperature deviation rate
Containers in those high TD rate trade lanes experience much longer ODTD
Trade Lanes with High Temperature Deviation Rate
40

## Slide 42
Charger Alarms vs. Voltage
Voltage has an effect on the number of charger alarms
When the supply voltage of both origin and destination countries are between 100V and 127V, the charger alarm rate is the highest (0.65%)
When the supply voltage of both origin and destination countries are between 220V and 240V, the charger alarm rate is the lowest (0.32%)
The container chargers are twice as likely to failure when the supply voltage is between 100V-127V
Failure Alarms Findings
41

## Slide 43
Compressor Alarms vs. Season
In the Chi-squared test, we have observed a statistically significant seasonal effect on the compressor alarm rate
Containers experience more compressor alarms in summer than other seasons
There is a significantly higher compressor alarm rate of 0.44% in the summer
Failure Alarms Findings
42

## Slide 44
Compressor Alarms Rate vs. Delta Temperature
Compressor alarm rate goes up as the delta temperature climbs. Especially after the temperature reaches above 15°C, the compressor alarm rate climbs quickly.
Failure Alarms Findings
43

## Slide 45
Compressor Alarms Rate vs. Out of Designed Temperature Duration
It seems that after total 4 hours of experiencing out of designed temperature, there is a big jump in the compressor alarm rate
Failure Alarms Findings
44

## Slide 46
Compressor Alarms Rate vs. Power Step Mean (Cooling)
A critical value of power step mean of 2, after which there is a big jump in the compressor alarm rate, is observed
Failure Alarms Findings
45

## Slide 47
Compressor Alarms Rate vs. Power Step Mean (Cooling)
Especially after the number of door openings reaches 6 time or more, there is a big jump in the compressor alarm rate
Failure Alarms Findings
46

## Slide 48
Heater Alarms vs. Season
Heater alarms are more likely to occur in summer
There is a significantly higher heater alarm rate of 0.2% in the summer.
Failure Alarms Findings
47

## Slide 49
Heater Alarms vs. ODTD
It seems that after total 10 hours of experiencing out of designed temperature, there is a big jump in the heater alarm rate
Failure Alarms Findings
48

## Slide 50
Heater Alarms vs. Number of Door Openings
As the number of door openings increases, the heater alarm rate tends to climb, and when the number of door openings pass 4, there is big jump of the heater alarm rate
Failure Alarms Findings
49

## Slide 51
Total Failure Alarms vs. Shipment Duration
The longer the shipment duration is, the higher the compressor total alarm rate is especially after the shipment duration is above 500 hours.
Failure Alarms Findings
50

## Slide 52
Total Failure Alarms vs. Battery Level
Total alarm rate tends decreases as the battery increases
Maintaining a high battery level throughout the shipments can help to decrease total parts failure alarms rate
Failure Alarms Findings
51

## Slide 53
Training and Validation AUC Score Progression of Logistic Regressions
Predictive Model Findings
52

## Slide 54
Training and Validation Loss and AUC Score Progression of XGBoost
Predictive Model Findings
53

## Slide 55
Training and Validation Loss and AUC Score Progression of ANN
Predictive Model Findings
54